Gluing a carcass together

Sash cramps are used to hold carcasses, frames and joints together while the glue sets. They are even used while welding large metal frames together.

- The bench should be cleared of all tools and before the wood is glued together the bench top should be covered with newspapers to catch the glue drips.

- Wet rags need to be at hand to wipe off the excess glue.

- The sash cramps should be opened to the required length making sure that they are free of dried glue from previous work.

- The cramps will damage the surface or edges of the wood by creating indentations, which may prove difficult to remove. To prevent this from happening cushion blocks should be made. The cushion blocks are placed between the jaws of the cramp and the wood surface.

Sash cramps used to hold a frame whilst it is gluing